## Slide 1: Integración de sistemas CMOS
Martín Carrá / Hernán Romero / Mariano García Inza / Benjamín Reyes / Patricio Pérez Preiti / Pablo Gardella

## Slide 2: Presentación de la materia

## Slide 3: Objetivo de la materia
Comprender cómo, a partir de una serie de necesidades, se generan requisitos ('requirements') y restricciones ('constraints'), y cómo estos sirven como base para conceptualizar y desarrollar un circuito de señal mixta en su nivel superior ('top level'). Este proceso debe considerar las interacciones del circuito con el entorno externo, asegurando que cumpla con los requisitos funcionales y de compatibilidad definidos.

## Slide 4: Programa sintético
Introducción a la ingeniería en sistemas
Sensores CMOS
Circuitos de Interfaz
Conversores ADC / DAC
Arquitectura de IC de señal Mixta
Requerimientos y protecciones ESD
Introducción a EMC
Martín Carrá
Hernán Romero / Mariano García Inza
Hernán Romero / Mariano García Inza
Benjamín Reyes
Martín Carrá / Hernán Romero
Patricio Pérez Preiti
Pablo Gardella

## Slide 5: Staff Docente
Ing. Martín Carrá.
Ing. Hernán Romero.
Dr. Ing. Mariano García Inza.
Dr. Ing. Benjamín Reyes
Ing. Patricio Pérez Preiti.
Ing. Pablo Gardella.

## Slide 6: Staff Docente
Ing. Hernán Romero
Academic Milestones
Engineering Degree (1992– 1999):
  Graduated as an Electronic Engineer from the University of Buenos Aires, Faculty of Engineering.
Specialized Training in CMOS Technology:
  Advanced Analog Design Technique MEAD course, including ultra-low voltage design.
Specialized Training in Delta-Sigma Design:
  Practical approaches to Delta-Sigma design MEAD course
  Continuous Time Delta Sigma design MEAD course.
Professional Milestones
Analog Design Engineer at Allegro Microsystems (2001 –2004)
  Design of Analog and Mixed-signal Hall effect IC sensors for linears, digital position and GTS apps.
Principal IC Design EngineerPrincipal IC Design Engineer (2004-2010)
  Lead Designer of Analog & Mixed Signal Hall effect IC sensors, focused on linear sensors for automotive and current sensor apps, in CMOS and BICMOS processes.
Advanced Sensors Technologies Design Manager - Sr IC Design Engineer (2010-2020)
  Product development group manager / IC design engineer of Analog & Mixed Signal Hall effect Linear sensors, from architecture development to circuit design.
Innovation Product Acceleration Design Manager (2020-2022)
  Prototype development for new Technologies.
Senior Member of Technical Staff, Design – Innovation (2022-2023)
  Prototype development and feasibility for new Technologies.
Distinguished Member of Technical Staff, Analog Design (present)
  Prototype development and feasibility for new Technologies.
Autor of 52 published patents in the US
  Two Allegro Innovation Awards (2017: US 9389060 & 2022: US11047933):

## Slide 7: Programa sintético
Introducción a la ingeniería en sistemas
Sensores CMOS
Circuitos de Interfaz
Conversores ADC / DAC
Arquitectura de IC de señal Mixta
Requerimientos y protecciones ESD
Introducción a EMC
Martín Carrá
Hernán Romero / Mariano García Inza
Hernán Romero / Mariano García Inza
Benjamín Reyes
Martín Carrá / Hernán Romero
Patricio Pérez Preiti
Pablo Gardella

## Slide 8: Agenda Sensores CMOS
Dyanmic Cancellation Techniques
Autozero vs Chopping
High Level Comparison
Auto-zero Amplifiers
Chopping Stabilization
Chopper-Stabilized Amplifier

## Slide 9: Interface Circuits

## Slide 10: Dynamic offset Cancellation

## Slide 11: Autozero vs Chopping

## Slide 12: Autozero Amplifiers
(Vores = Vos’-Vos)

Vos’
_
Vin*A

## Slide 13: Autozero Limitations : Noise Aliasing
Vn+
1
Noise model
If vn assumed stationary

## Slide 14: Autozero Limitations : Noise Aliasing
Flicker noise USF
White noise USF
1/f noise is removed though
1/f replicas lie out of band
(Noise BW)

## Slide 15: Autozero Limitations : Summary
Vn+
In Band WN power is Increased (aliasing)
Residual offset is high for low A
Output is not valid all the time (no continuous-time output)
OFFSET & 1/f noise are completely removed (fch > fK=1/f)
Effective gain is higher than conventional amplifier

## Slide 16: Chopper-Stabilization

## Slide 17: Chopper Stabilization Concept
f / fch
1
VSIG
3
5
Modulated offset & 1/f
VSIG
1
f / fch
3
5
Modulated offset & 1/f
VSIG
1
f / fch
3
5
SF
VOFF + VN
VSIG
VOFF
VSIG
(1)
(2)
(3)
(4)
fA>> fch
1
3
5
f / fch
Modulated signal
VOFF + VN
1/f
BA
smoothing filter
A(f)
Modulation process

## Slide 18: Chopper Stabilized Amplifiers – Concept II
fk ~ 2KHz
Note: scope plots scale: 2sec/div
Not only offset is removed !

## Slide 19: Chopper Stabilization Concept III
This is a modulation process…
WN is then modulated too…
So baseband noise is again aliased!, but (as opposed to AZ) …
Chopper’s output PSD
all input signal spectra replicas are weighted such that the sum of all coefficients equals 1
If vn assumed stationary

## Slide 20: Chopper Stabilization Limitations
Rule of thumb  fA > 5 fch
or
CLOSED LOOP AMPLIFIER (High loop gain can tolerate LF gain loses)
Another example…

## Slide 21: Chopper Stabilization Limitations
For a 2-stage chopped amp
Proportional to
offset & fLPF/fCH ratio
1-pole LPF

## Slide 22: Chopper Stabilization Limitations
What causes residual offset?
Charge injection at the input chopper switches = f(fch) !!
RESOFF & CM errors
1
f / fch
3
5
2
4
f / fch
Modulated RESOFF & CM errors
1
3
5
2
4

## Slide 23: Chopper Stabilization Limitations
IMPORTANT
The residual offset is proportional to the chopping frequency!
Input-referred Amplifier’s Residual offset

## Slide 24: Chopper Stabilization Summary
Noise before chopping
White noise
Noise after chopping
1
f/fch
ripple
f-3dB= 1/OSR
fK: 1/f corner frequency
CT LPF
(N x 20dB/dec roll off)
Modulated 1/f noise
Delay Increases with fCH/fLPF (OSR)
Residual offset  fch
HF Ripple proportional to (lower effective gain):
  offset voltage
  1/OSR
OFFSET & 1/f noise are completely removed (fch > fK=1/f)
In Band WN power is NOT Increased

## Slide 25: Chopper Stabilization Summary
TRADE OFFS | 
(1) | Residual noise (band-limited White noise + Ripple (harmonic noise)) vs. SNR / Dynamic range / Delay
(2) | Residual Offset vs. Efficiency
(3) | BW limitation (speed) vs. Gain accuracy (Temp-co, linearity …)

## Slide 26: Dynamic offset compensation comparison

## Slide 27: DOC High Level Comparison
Summarized performance of different offset cancellation techniques
 | Bandwidth (delay) | Offset drift | 1/f noise | White noise | Continuous time | Effective gain
Trimming | N | - | - | N | + | +
Auto-zeroing | N | + | + | - | - | +
Chopping | -1 or N2 | + | + | N | +1 or N2 | N / +3
N = Neutral
1CT filtering or feedback ripple reduction techniques
2Tuned filtering techniques
3 Offset compensation / stabilization techniques – Closed loop chopped amplifiers

## Slide 28: Chopper-stabilized Amplifiers

## Slide 29: Chopper-Stabilized Amplifiers Fighting Limitations
  Fighting Bandwidth
    Usual approach
    Currents are faster than voltages
  Fighting ripple
    CT filtering
    (DT) Tuned filtering: Track and hold demodulation
    (DT) Tuned filtering – revisited: low noise approach
    Offset compensation (feedback)
    Offset stabilization
    Chopped auto-zero
  Fighting residual offset
    Nested chopping
    Guard-banding
    Bandpass filtering

## Slide 30: Chopper-Stabilized Amplifiers Fighting Bandwidth
How can we alleviate DC gain reduction due to limited BW?
Closed loop amps
DC gain loses are not noticed
High speed chopping
Is it required to chop all gain stages ?
Slew rate requirement highly reduced
Slew rate might be compromised
Currents are “faster than voltages”
Chopped cascodes

## Slide 31: Chopper-Stabilized Amplifiers Closed Loop Amplifiers
NEGATIVE FEEDBACK: high loop gain can tolerate LF gain loses without significantly affecting closed loop gain.
Aol
Aoleff2
Acl
VOFF + VN
VSIG
SF
f
f
fchop
fchop
fchop
Aoleff1
Design Problem !: Very high slew rate requirements
dV/dT  VSIG & fchop

## Slide 32: Chopper-Stabilized Amplifiers High Speed Chopping
VOFF + VN
VSIG
SF
f
f
gm1
gm2
So….
? Gm2 is left outside chopper: Its offset contribution is negligible if Gm1*(Ro1//Ri2) = A1 is large (usually the case) since
 Slew rate requirements are reduced Gm2*RL = A2 times !!
 Stabilization stage provides a first LPF means !  SF is relaxed

## Slide 33: Chopper-Stabilized Amplifiers High Speed Chopping II
Example of Gm1
VOFF + VN
VSIG
SF
f
f
gm1
gm2

## Slide 34: Chopper-Stabilized Amplifiers High Speed Chopping II
Example of Gm1
VOFF + VN
VSIG
SF
f
f
gm1
gm2

## Slide 35: Chopper-Stabilized Amplifiers High Speed Chopping III
 Gm1 becomes a wide-band stage (not limited by following stabilization stage bandwidth)
 fch can be increased !
(until Vresoff hurts)
 Cascode devices provides a first filtering means.
What happens if demodulation switches are moved to LOW IMPEDANCE nodes?

## Slide 36: Chopper-Stabilized Amplifiers Fighting Limitations - Overview
  Fighting Bandwidth
    Usual approach
    Currents are faster than voltages
  Fighting ripple
    CT filtering
    (DT) Tuned filtering: Track and hold demodulation
    (DT) Tuned filtering – revisited: low noise approach
    Offset compensation (feedback)
    Offset stabilization
    Chopped auto-zero
  Fighting residual offset
    Nested chopping
    Guard-banding
    Bandpass filtering

## Slide 37: Chopper-Stabilized Amplifiers Fighting Ripple - Overview
Why do we want to further reduce ripple?
  Relaxes post-chopper LPF (can be integrated)  allows for lower OSR  Signal delay can be reduced
  Improves dynamic range
How can we further reduce ripple ?
CT filtering
Low pass (Conventional chopping)
High pass
Tuned Filtering
T&H demodulation
Offset compensation
Baseband offset
Low noise
Offset stabilization
Modulated offset
Auto-zero
Chopper
Chopped Auto-zero
Discrete or Continuous time output

## Slide 38: Chopper-Stabilized Amplifiers Fighting Ripple – HPF topology
Modulated signal
VOFF + VN
1/f
(2)
Modulated offset & 1/f
VSIG
1
f / fch
3
5
(5)
VOFF
VSIG
(1)
VOFF + VN
VSIG
SF
fo << fch
HPF
(4)
(3)
Modulated signal
VOFF + VN
1/f
Modulated signal
VOFF + VN
In band
WN PSD is NOT increased 
Out of band
Ripple: only proportional to fHPF, not to offset anymore
Delay: proportional to 1/fHPF

## Slide 39: Chopper-Stabilized Amplifiers Fighting Ripple – Tune filtering – T&H demodulation
VOFF
VSIG
(1)
(2)
(3)
(5)
Sampling is done here…
VSIG
VOFF + VN
1
3
5
f / fch
Modulated signal
1/f
Modulated offset & 1/f
1
3
5
2
4
f / fch
…and then demodulated…
(Inverting phase)
f / fch
1
3
5
2
4
… and finally averaged
(Aliasing takes place!)
Assuming fA>>fch 
(This is the ripple we want to kill!)
VOFF + VN
VSIG
SF
(smoothening)
Track & hold demodulation

## Slide 40: Chopper-Stabilized Amplifiers Fighting Ripple – Tune filtering – T&H demodulation (cont)
VOFF + VN
VSIG
SF
(smoothening)
Track & hold demodulation
In band
WN aliasing ! 
Out of Band
Ripple:
Delay: only limited to smoothing filter 
Virtually eliminated 
Independent of circuit parameters 

## Slide 41: Chopper-Stabilized Amplifiers Fighting Ripple – Tune filtering – Low noise approach
VOFF
VSIG
(1)
(2)
(3)
(4)
Sinc filter
2
(5)
Sampling is done here
Modulated offset & 1/f
VSIG
1
f / fch
3
5
1
3
5
2
4
f / fch
f / fch
1
3
5
2
4
or here
And averaged out here
Conventional chopper-stabilized amplifier
SF
VOFF + VN
VSIG

## Slide 42: Chopper-Stabilized Amplifiers Fighting Ripple – Tune filtering – Low noise approach (cont)
Sinc filter
2
SF
VOFF + VN
VSIG
CKSA
CKSB
CKR
TCK
TCK
TCK

## Slide 43: Chopper-Stabilized Amplifiers Fighting Ripple – Tune filtering – Low noise approach (cont)
Sinc filter
2
SF
VOFF + VN
VSIG
In band
WN PSD is NOT increased 
Out of band
Ripple:
Delay: only limited by AAF 
Virtually eliminated 
Independent of circuit parameters 

## Slide 44: Chopper-Stabilized Amplifiers Fighting Ripple – Baseband Offset compensation (RRL)
Conventional chopper-stabilized amplifier
Modulated offset & 1/f
VSIG
1
f / fch
3
5
1
3
5
VOFF + VN
1/f
VOFF + VN
Modulated signal
VOFF + VN
1/f
Vo
fo<<fch
+
-
LP filter
SF
Voff
t
Time response

## Slide 45: Chopper-Stabilized Amplifiers Fighting Ripple – Bandpass Offset compensation (RRL)
Conventional chopper-stabilized amplifier
Modulated offset & 1/f
VSIG
1
f / fch
3
5
1
3
5
VOFF + VN
1/f
Modulated offset & 1/f
1
f / fch
3
5
Voff
t
Time response
fo=fch
+
-
Vo
Tuned BP filter
VOFF + VN
SF

## Slide 46: Chopper-Stabilized Amplifiers Fighting Ripple –Offset compensation (cont)
Vo
fo<<fch
+
-
LP filter
SF
VOFF + VN
fo=fch
+
-
Vo
Tuned BP filter
VOFF + VN
SF
In band
WN PSD is NOT increased 
Out of band
Ripple:
Delay:
Only proportional to 1/Aol 
WN Aliasing occurs if feedback tuned filter is used to reduce delay 
Prop. to loop speed 

## Slide 47: Chopper-Stabilized Amplifiers Fighting Ripple –Offset stabilization
GOAL: Compensate for main amplifier’s offset
+ Continuous-time signal path
- Only for closed loop amplifiers
Vo
Compensation amp
VOFF + VN
+
-
Comp amp:
Chopper offset-stabilized
Auto-zero offset-stabilizied

## Slide 48: Chopper-Stabilized Amplifiers Fighting Ripple –Offset stabilization (cont)
Two forward paths  pole-zero doublets
Vo
Compensation amp
VOFF + VN
+
-
Main Amp
K/(s+p1)
Comp Amp
K/(s+p2)
Output stage
+
 Stability issues!
Hybrid nested Miller
-gm2
-gm1
-gm5
-gm4
-gm3
Without HNM comp
With HNM comp
Requires BWMP=BWCP

## Slide 49: Chopper-Stabilized Amplifiers Fighting Ripple – Chopper+AZ
Chopping frequency - fch
Noise PSD [V]
Voff +Vn
(a) No chopping, no AZ
Autozeroing frequency - fAZ
Voff +Vn are decreased
Baseband noise increased
Noise PSD [V]
(b) No chopping, with AZ
Modulated Voff +Vn
Noise PSD [V]
Voff +Vn are decreased
Modulated noise increased
(c) With chopping, no AZ
Noise PSD [V]
Voff +Vn are decreased
Baseband noise is decreased
Modulated noise increased
Chopping frequency - fch
fAZ + fch
(d) With chopping, with AZ

## Slide 50: Chopper-Stabilized Amplifiers Fighting Ripple - Summary
 |  | Ripple cancellation (out of band noise) | Noise aliasing (in band noise) | Delay | CT output | Closed /Open-loop topology | Observations
CT filtering | LPF | - | + | - | Yes | Both | Involves long delays to further reduce ripple
 | HPF | -/+ |  |  |  |  | Slightly better than LPF since ripple is not proportional to offset
Tuned filtering | T&H demod. | + | - | + | Yes | Both | Delay is only related to smoothening LPF
 | Low noise |  | + |  |  |  | Delay is only related to AAF, which can be (marginally) fo=fch
Offset comp. | Baseband offset | + | +(*) | - | Yes | Ideally both. CL only in practice | Delay is proportional to loop speed (*) Could be poor if discrete time notch filter is used inside the loop
 | Mod. Offset |  |  |  |  |  | 
Offset stabilization | Chopper | -/+ | + | - | Yes | CL only. Stabilization is complex. | Residual ripple from compensation path needs to be minimized
 | AZ |  | - |  | No |  | Folds back baseband noise of compensating amplifier
Chopped AZ | Single | + | +(*) | + | No | Ideally both. CL only in practice | 
 | Ping-Pong |  |  | + | Yes |  | (*) Further removed by chopper

## Slide 51: Chopper-Stabilized Amplifiers Fighting Limitations - Overview
  Fighting Bandwidth
    Usual approach
    Currents are faster than voltages
  Fighting ripple
    CT filtering
    (DT) Tuned filtering: Track and hold demodulation
    (DT) Tuned filtering – revisited: low noise approach
    Offset compensation (feedback)
    Offset stabilization
    Chopped auto-zero
  Fighting residual offset
    Nested chopping
    Guard-banding
    Bandpass filtering

## Slide 52: Chopper-Stabilized Amplifiers Fighting Residual Offset
What causes residual offset?
How can residual offset be reduced?
Band pass filtering
Currents are “faster than voltages”
Guard banding
Oversampling ratio can be maximized
Chopped cascodes
Nested chopping
Is it required to chop all gain stages ?
Slew rate requirement highly reduced

## Slide 53: Chopper-Stabilized Amplifiers Fighting Residual Offset – Bandpass Filtering
“A fully integrated, untrimmed CMOS instrumentation amplifier with sub-microvolt offset” – Menolfi et. Al – IEEE JSSC March 1999
Back end
amplifier
front end
amplifier
fo=2fCLK
f / fch
Modulated RESOFF & CM errors
1
3
5
2
4
f / fch
1
3
5
2
4
RESOFF & CM errors
1
f / fch
3
5
2
4
Requires very good matching between fo and fch

## Slide 54: Chopper-Stabilized Amplifiers Fighting Residual Offset – Nested Chopper
“A CMOS Nested-Chopper Instrumentation Amplifier with 100-nv Offset” - Bakker et.al – IEEE JSSC Dec 2000
Requires tighter LPF f-3dB < flow
f / fch
Modulated @ fhigh
RESOFF & CM errors
1
3
5
2
4
RESOFF & CM errors
1
f / fch
3
5
2
4
Modulated @flow
RESOFF & CM errors
1
f / fch
3
5
2
4

## Slide 55: Chopper-Stabilized Amplifiers Fighting Residual Offset – Guardbanding
A. Bilotti, G. Monreal, “Chopper-stabilized amplifiers with a track-and-hold signal demodulator,” IEEE Trans. On Circuits & Systems-I, April 1999
Slightly worse noise performance.
Output is not available during guard band
f / fch
Modulated RESOFF & CM errors
1
3
5
2
4

## Slide 56: Wrap Up

## Slide 57: Static Offset Cancellation: This involves permanent adjustments to compensate for initial offset errors. Hall Plates (Dual/Quads): Uses multiple Hall plates with opposing sensitivities to cancel out offset. Accuracy relies on matching between the plates. More current is consumed. Thermal noise is reduced, but flicker noise remains. Amplifiers (Trimming): A digital-to-analog converter (DAC) is used to trim the amplifier's offset. The accuracy of this method is limited by the DAC resolution (typically not effective beyond 5 bits). Various trimming methods are available (laser trimming, fusible links, PROM). Dynamic Offset Cancellation: This involves continuous modulation and signal processing techniques to dynamically eliminate offset and 1/f noise. Hall Plates (Current Spinning): A single Hall plate is used, but the bias current is cycled through different phases to modulate the offset. This effectively moves the offset away from DC, allowing it to be filtered out. Amplifiers (Auto-Zeroing, Chopping, Offset Stabilization): Various techniques are described, including: Auto-Zeroing: Periodically samples and subtracts the offset. Leads to a sampled data output. Chopping: Modulates the signal to a higher frequency, shifting the offset and 1/f noise away from DC, allowing for filtering. Results in a continuous-time output but introduces ripple (harmonic noise) and signal delay. Offset Stabilization: Uses a secondary compensation amplifier to cancel the main amplifier's offset in a closed-loop configuration.

## Slide 58: Trade-offs Residual Noise vs. SNR/Dynamic Range/Delay: Dynamic techniques, while effective at reducing offset and 1/f noise, often introduce residual noise (e.g., ripple in chopping). The choice of filtering methods (CT filtering, feedback, tuned filtering) significantly impacts the trade-off between residual noise, signal-to-noise ratio (SNR), dynamic range, and signal delay. Residual Offset vs. Efficiency: Static offset cancellation can be less efficient in terms of power consumption, especially when using multiple Hall plates. Dynamic methods can achieve better efficiency. BW Limitation (Speed) vs. Gain Accuracy: Chopping, while effective for offset cancellation, can limit the bandwidth of the amplifier due to the chopping frequency and the need for low-pass filtering. This limitation affects the speed of the amplifier's response. Additionally, achieving precise gain accuracy can be more challenging with chopping techniques

## Slide 59: Tareas
implementación circuito de bias y current spinning de Hall plate
  Modelado funcional (componentes ideales) por bloques en cadence.
    Estos bloques, luego de ser verificado a nivel funcional, serán reemplazados por su versión a nivel de transistores.
    Incluir Fuentes de offset en el modelo de transductor para comprobar la correcta modulación de estas en el proceso de choppeado
    Incluir coeficientes de temperatura en generación de tensión / Corriente y parámetros principales según corresponda.
  Modelado circuital
    implementación a nivel de transistores del circuito de bias.
    Detallar tamaño de transistores usados para la conmutación de la Hall plate (W,L)
  Para ambos modelos
    Simular punto de operación y transitorios de conmutación verificando salida diferencial de la celda Hall acorde al campo aplicado (sensitivity check), y tensión o Corriente de bias.
implementación de amplificador choppeado de interfaz de Hall
  Modelado funcional (componentes ideales) de un amplificador choppeado.
    verificación funcional (transitorios) con y sin offset aplicados.
    Verificación de ganancia y offset residuales.
    Incluir coeficientes de temperatura en parámetros principales según corresponda.
  Modelado circuital
    verificación funcional (transitorios) con y sin offset aplicados.
    Verificación de ganancia y offset residuales.
    Incluir coeficientes de temperatura en parámetros principales según corresponda.
    Detallar tamaño de transistores usados (WL) y topología usada para etapa de entrada y salida del amplificador.
  Para ambos modelos
    Simular punto de operación y transitorios de conmutación verificando salida diferencial acorde al campo aplicado

## Slide 60: References
  “Circuit techniques for reducing the Op-Amp imperfections: Autozeroing, Correlated Doubling Sampling and Chopper stabilization” – C. Enz, et. al. – Proceedings of the IEEE. Nov. 1996
  “Power, accuracy and noise aspects in CMOS mixed-signal design” – M.A.T. Sanduleanu - ISBN: 90-3651265-4 - ©1999, M.A.T. Sanduleanu
  “CMOS single chip electronic compass with microcontroller “– Schott, et.al - IEEE JSSC Dec 2007
  “Monolithic Magnetic Hall sensor using dynamic quadrature offset cancellation” – A. Bilotti, G. Monreal, R. Vig – IEEE JSSC June 1997
  Chopped Hall effect Sensor – G. Monreal, H. Romero – US7425821
  “A Chopped Hall Sensor With Small Jitter and Programmable “True Power-On” Function“ – Motz et.al – IEEE JSSC Jul. 2005
  “Auto-correction feedback for Ripple Suppression in a Chopper Amplifier” – Kusuda – IEEE JSSC Aug 2010 – p. 1436-1445.
  “A Chopper Current-Feedback Instrumentation Amplifier with a 1mHz 1/f Noise Corner and an AC-Coupled Ripple reduction loop” – R. Wu, et.al. - IEEE JSSC – Dec 2009 – p. 3232-3243
  “A CMOS Chopper Offset-Stabilized Opamp “ – Witte et. al. – JSSC IEEE Jul 2007
  “Chopper stabilization of MOS Operational Amplifiers using feed-forward Techniques” – Coln – IEEE JSSC Dec 1981, p. 745 -748.
  “Frequency stabilization of chopper-stabilized amplifiers”. J. Huijsing, et.al. – US 7209000.
  “Switched capacitor Notch filter “– H. Romero – US 7990209
  “A 1V low noise CMOS amplifier using noise reduction technique of Autozeroing and chopper stabilization” - Yoshihiro Masui, et. al. – Hiroshima University.

## Slide 61: Until next Friday…